## Slide 1
LIDARGO: standardization
Stefano Letizia
04/02/2024

## Slide 2: Standardization: overview

## Slide 3: Pre-conditioning
Raw angles would contain backswipe, when the lidar scans fast to return to home position
Selected angles would contain irregular beams outside the regular geometry
Backswipe is identified by imposing limits on the azimuth and elevation steps, calculated both with forward and backword finite differences:
Regular vs irregular beams are flagged by checking their distance from the closest regular beam:
ang_tol
Angles are regularized by shifting them to the closed regular angle.
Regularized angles only include angles corresponding to the regular geometry
Expected locations (, ) are identified as the most likely in the 2D p.d.f. of azimuth and elevation:

## Slide 4: Pre-conditioning
2D pdf for the selection of the regular angles
Angles classification for a PPI scan

## Slide 5: Quality control: pre-filter
range_min
range_max
ground_level
Geometrical constraints
Physical constraints
SNR
rws_min
rws_max
snr_min
The pre-filter applies general geometrical and physical limits to the data that do not depend on the flow. It proceeds the subsequent dynamic filter and speeds up/facilitates its processing.

## Slide 6: Quality control: dynamic filter
and SNR data are binned into 4D spacetime bins
dz
dx
dy
dtime
the bin-median is calculated, and its statistical significance checked
the normalized and SNR are calculated as fluctuations over the local median and their 2D p.d.f analyzed
SNR’

## Slide 7: Quality control: dynamic filter
rws_norm_limit
min_probability_range
max_probability_range
Data are rejected if their probability in the plane is below threshold
To find the threshold, the variability of as a function of probability is checked by calculating the range of max_percentile minus min_percentile in N_probability_bins bins
The threshold is defined as the probability where the bin-variability exceeds the fraction rws_norm_increase_limit of the whole range of
The threshold is constrained within min_probability_range and max_probability_range
Finally, scarcely populated bins where a fraction more than local_scattering_min_limit of points where entirely rejected are discarded
max_percentile - min_percentile

## Slide 8: Quality control: examples

## Slide 9: Standardization
scanID=1
scanID=2
scanID=3
The scan repetition is found by checking the nearest previous time the beams scan the initial angular position
The beam repetition (i.e. the scan trajectory in time) is found by the median time it takes for the beams to reach every angular position, which is a tricky task since many beams may have been filtered out at this stage.
Angle
Finally, scans a classified in three categories that are useful for plotting:
PPI
RHI
3D